| NOTE : Work must be performed in accordance with this SWMS. This SWMS must be kept and be available for inspection until the high risk construction work to which this SWMS relates is completed. If the SWMS is revised, all versions should be kept. If a notifiable incident occurs in relation to the high risk construction work in this SWMS, the SWMS must be kept for at least 2 years from the date of the notifiable incident. |
| --- |
| (PCBU Name, ABN, Office Address and Phone) | Principal Contractor (PC) | (Name, ABN, Office Address) |
| Works Manager: Contact phone: |  | Date SWMS provided to PC: |  |
| Work activity: | Install/remove stair void protection | Workplace location: |  |
| High risk construction work: | X Risk of a person falling more than 2 metres | ( Work on a telecommunication tower | ( Demolition of load-bearing structure |
|  | ( Likely to involve disturbing asbestos | ( Temporary load-bearing support for structural alterations or repairs | ( Work in or near a confined space |
|  | ( Work in or near a shaft or trench deeper than 1.5 m or a tunnel | ( Use of explosives | ( Work on or near pressurised gas mains or piping |
|  | ( Work on or near chemical, fuel or refrigerant lines | ( Work on or near energised electrical installations or services | ( Work in an area that may have a contaminated or flammable atmosphere |
|  | ( Tilt-up or precast concrete elements | ( Work on, in or adjacent to a road, railway, shipping lane or other traffic corridor in use by traffic other than pedestrians | ( Work in an area with movement of powered mobile plant |
|  | ( Work in areas with artificial extremes of temperature | ( Work in or near water or other liquid that involves a risk of drowning | ( Diving work |
| Have workers been consulted about the SWMS? Note: Consultation with Health and Safety Representatives (HSRs) should be undertaken where there is a HSR at a workplace | ( YES ( NO |
| Person/s responsible for ensuring compliance with SWMS: |  | Date SWMS received: |  |
| What measures are in place to ensure compliance with the SWMS? |  |
| Person responsible for reviewing SWMS control measures: |  | Date SWMS received by reviewer: |  |
| How will the SWMS control measures be reviewed? |  |
| Review date: |  | Reviewer’s signature: |  |

| What are the tasks involved? | What are the hazards and risks? | What are the control measures? |
| --- | --- | --- |
| List the work tasks in a logical order. | Identify the hazards and risks that may cause harm to workers or the public. | Describe what will be done to control the risk. What will you do to make the activity as safe as possible? |
| Works planning | Structural Failure | Inspect all structures where Void protection/platform are to be installed: Ensure all joist and floor sheeting and the Void protection/platform is structurally secure. If not structurally secure, DO NOT install until structurally secure |
| Preparation of Site | Electrocution through exposure to power lines or energised electrical assets | Prior to commencing work, check for overhead power lines including domestic service and lead in power lines. Ensure a VESI Permit to work is adhered to if working within a NO GO Zone Ensure all works remain clear of any energised electrical assets (construction site power supply and wiring) |
| Assembling, moving and Installing components | Manual Handling – Musculoskeletal injuries | Ensure delivery vehicles are unloaded in designated areas Deliver materials as close as possible to work location – use mechanical means if practicable Only lift within own capacity and use two person move/lift if required |
| Installing System | System Failure | Each void platform system has different requirements – refer to system manual for system requirements for component assembly and fixings Check all components prior to install to ensure they are in serviceable condition and satisfactory for use. |
|  | Falling into void area Manual Handling – Musculoskeletal injuries | Do not install the system from the platform level, it must be installed from below. Installation of the system to be completed from a suitable industrial rated platform ladder Use two person lift for larger decks or awkward lifts |
|  | Falling Objects striking others | Ensure persons, including any other worker/s involved in the task stand clear when decks and poles are being lifted into place Clear away debris that could potentially be knocked into void area. |
| Installing Ladder | Ladder unstable or tipping | Ensure ladder is sitting inside the ladder bracket and secured |
| Accessing the Platform | Fall from Height | Before accessing the platform ensure the deck is secured and all poles/fittings are secured to the structure When installing deck clamps, ensure deck holders/keepers are installed to the pole so that the platform and Deck/s can be separated safely to install deck clamps or other method of ensuring the deck/s are secure Once Deck Clamps are installed Deck Keepers can be installed tight against the platform Do not access the void platform where there is a risk of fall (eg a window opening) unless edge protection has been installed Do not expose yourself or others to any unprotected edge |
| Dismantling Void Platform | All hazards outlined above | Inspect the Void Platform prior to dismantle to ensure the system has not been tampered with and is still structural sound Ensure that others are not working above prior to dismantle, establish an exclusion zone if required Dismantle Void Platform in reverse order to installation procedures using all control measures above |

| Name of Worker/s | Worker signature/s |
| --- | --- |
| Date SWMS received by workers |  |

PLEASE NOTE: It may be necessary to use more than one page to complete an adequate safe work method statement (SWMS).