| (PCBU Name, ABN, Office Address and Phone) | Principal Contractor (PC) | (Name, ABN, Office Address) |
| --- | --- | --- |
| Works Manager: Contact phone: |  | Date SWP provided to PC: |  |
| Work activity: | General carpentry work below 2m – House frame single story | Workplace location: |  |
| High risk construction work: | ( Risk of a person falling more than 2 metres | ( Work on a telecommunication tower | ( Demolition of load-bearing structure |
|  | ( Likely to involve disturbing asbestos | ( Temporary load-bearing support for structural alterations or repairs | ( Work in or near a confined space |
|  | ( Work in or near a shaft or trench deeper than 1.5 m or a tunnel | ( Use of explosives | ( Work on or near pressurised gas mains or piping |
|  | ( Work on or near chemical, fuel or refrigerant lines | ( Work on or near energised electrical installations or services | ( Work in an area that may have a contaminated or flammable atmosphere |
|  | ( Tilt-up or precast concrete elements | ( Work on, in or adjacent to a road, railway, shipping lane or other traffic corridor in use by traffic other than pedestrians | ( Work in an area with movement of powered mobile plant |
|  | ( Work in areas with artificial extremes of temperature | ( Work in or near water or other liquid that involves a risk of drowning | ( Diving work |
| Have workers been consulted about the SWP? Note: Consultation with Health and Safety Representatives (HSRs) should be undertaken where there is an HSR at a workplace | ( YES ( NO |
| Person/s responsible for ensuring compliance with SWP: |  | Date SWP received: |  |
| What measures are in place to ensure compliance with the SWP? |  |
| Person responsible for reviewing SWP control measures: |  | Date SWP received by reviewer: |  |
| How will the SWP control measures be reviewed? |  |
| Review date: |  | Reviewer’s signature: |  |

| What are the tasks involved? | What are the hazards and risks? | What are the control measures? |
| --- | --- | --- |
| List the work tasks in a logical order. | Identify the hazards and risks that may cause harm to workers or the public. | Describe what will be done to control the risk. What will you do to make the activity as safe as possible? |
| Workers are competent in use of type of nail gun | Insufficient knowledge or experience to perform tasks that could lead to injury from carpentry hazards | This SWP is designed for use by a carpenter or competent person, or for workers under supervision of a carpenter or competent person *Note – This SWP uses house frame erection for a single-story structure as an example of general carpentry and can be used for any general ground level carpentry - for detailed safe use of tools and equipment, use and refer to a separate SWP for any specialised tool or equipment |
| Timber/prefabricated frames/trusses brought to site- Unloading equipment | Falling objects Manual handling – Musculoskeletal injuries | Prefabricated frames and trusses are to be unloaded using mechanical aid – forklift/vehicle loading crane SWMS required separately to this SWP Unload materials as close as practicable to work area to reduce manual handling Use two person lifts where manual handling of large objects is required Workers to lift only within their own physical capacity |
| Manual handling (general) | Manual handling – Musculoskeletal injuries | Use mechanical aids where practicable Use two person lifts as required for manual handling of large or awkward objects |
| Setting up materials and equipment | Slips trips and falls Crush hands, cuts or lacerations | Set up equipment on level ground. Avoid rough and difficult terrain Use applicable PPE when using saws and nail guns and other powered tools such as - safety glasses and hearing protection Use tools and equipment only that you are trained in – if unfamiliar then only use under instruction and supervision of a competent person Wear safety footwear Hang leads out of access ways on insolated hooks only Ensure that power supply is RCD protected |
| Laying first floor joist | Slips, trips and falls when carrying Fall from height (ladder or trestle under 2m) | Clear work area of debris and obstructions. Ensure assistance and team lift when placement of joists off ladder Work platform ladder or plank set up no more than 2m off working area Industrial grade ladder / work platform ladder or trestle with planks must be used. Do not over reach Back prop noggins if used for resting planks |
|  | Electric shock Cuts from power saw when cutting joist | Ensure power supply is RCD protected Test and tag electrical equipment Training/supervision in the use of a power saw. Ensure guarding is working and in place Training/supervision in the use of a nail gun. Ensure safe use – refer to separate SWP if required |
| Loading and placement of wall frames to the ground floor and top plate | Falls and trips when carrying frames Back and shoulder injury when standing frames Falls from height | Check weather conditions. Do not erect in high winds or rain Ensure clear access, work area is clear of debris and obstructions. Assess weight and use team lifting when required Before standing walls install timbers across window openings at 900mm off floor to create handrail. Avoid bump fire on nail guns except for floor install Electrical equipment test and tag Wear gloves and glasses installing metal bracing and clips Use two people to stand walls utilizing stopping blocks so walls don’t slide off top plate |
| Marking top plate for trusses | Falls from height | Use an industrial grade step ladder/Work platform or trestle planks from inside the house slab Ensure to reinforce noggins to hold planks correctly Do not overreach |
| Installation of trusses | Fall from height above 2m | This is an SWP for work under 2m. For install of trusses refer to separate SWMS for work above 2m |
| Storage of materials |  | Large carpentry works can last for several days or longer – ensure that all materials that need to be stored overnight are: Stack timber, frames, trusses or other timber, and materials on a dedicated lay down area /s Ensure that all materials remain clear of vehicle path or other trades/workers access/egress |
| Clean up | Housekeeping, slip trip, fall hazard Dust, sharp edges | Clean up all offcuts/waste at the end of each day, place in dedicated waste area or remove from site if required Wear dust mask if excessive dust, gloves and eye protection. |

| Name of Worker/s | Worker signature/s |
| --- | --- |
| Date SWP received by workers |  |

PLEASE NOTE: It may be necessary to use more than one page to complete an adequate safe work procedure (SWP).