| NOTE: Work must be performed in accordance with this SWMS. This SWMS must be kept and be available for inspection until the high-risk construction work to which this SWMS relates is completed. If the SWMS is revised, all versions should be kept. If a notifiable incident occurs in relation to the high-risk construction work in this SWMS, the SWMS must be kept for at least 2 years from the date of the notifiable incident. |
| --- |
| (PCBU Name, ABN, Office Address and Phone) | Principal Contractor (PC) | (Name, ABN, Office Address) |
| Works Manager: Contact phone: |  | Date SWMS provided to PC: |  |
| Work activity: | Concrete line pump | Workplace location: |  |
| High risk construction work: | ( Risk of a person falling more than 2 metres | ( Work on a telecommunication tower | ( Demolition of load-bearing structure |
|  | ( Likely to involve disturbing asbestos | ( Temporary load-bearing support for structural alterations or repairs | ( Work in or near a confined space |
|  | ( Work in or near a shaft or trench deeper than 1.5 m or a tunnel | ( Use of explosives | ( Work on or near pressurised gas mains or piping |
|  | ( Work on or near chemical, fuel or refrigerant lines | ( Work on or near energised electrical installations or services | ( Work in an area that may have a contaminated or flammable atmosphere |
|  | ( Tilt-up or precast concrete elements | ( Work on, in or adjacent to a road, railway, shipping lane or other traffic corridor in use by traffic other than pedestrians | X Work in an area with movement of powered mobile plant |
|  | ( Work in areas with artificial extremes of temperature | ( Work in or near water or other liquid that involves a risk of drowning | ( Diving work |
| Have workers been consulted about the SWMS? Note: Consultation with Health and Safety Representatives (HSRs) should be undertaken where there is an HSR at a workplace | ( YES ( NO |
| Person/s responsible for ensuring compliance with SWMS: |  | Date SWMS received: |  |
| What measures are in place to ensure compliance with the SWMS? |  |
| Person responsible for reviewing SWMS control measures: |  | Date SWMS received by reviewer: |  |
| How will the SWMS control measures be reviewed? |  |
| Review date: |  | Reviewer’s signature: |  |

| What are the tasks involved? | What are the hazards and risks? | What are the control measures? |
| --- | --- | --- |
| List the work tasks in a logical order. | Identify the hazards and risks that may cause harm to workers or the public. | Describe what will be done to control the risk. What will you do to make the activity as safe as possible? |
| Pre-Start – Consult on all of the task: preparation/core task activities/clean up | Mechanical hazards to workers in vicinity of concreting operations. | Ensure pump has dedicated and excluded work zone if practicable Ensure that others involved in the concreting operations have knowledge of concreting plan Consult in prestart meeting if required or is necessary |
| Preoperational check of all equipment to be used access ramps, traffic management equipment, plant, pipes and attachments. | Electrocution, rupture of pipe, collapse of ramp, Impact/ crushing injury from equipment failure. | Inspection of all equipment using checklists where required, check all cam locks - do not use if worn, if in doubt tag out of service. Use safety pins in cam lock for each join and secondary strap at pump end coupling. |
| Manage work zone | Public protection from concrete pumping hazards | Set up out of access to public if possible Erect public exclusion zone as per traffic/ pedestrian management plan Exclude all persons not in direct need for the pumping operations clear of the pump |
|  | Overhead power lines | Line pump only operation, do not extend any attachment into NO GO Zone If in NO GO Zone comply with Permit to Work conditions |
|  | Pump Vehicle stability, collapse, point loading | Ensure that pump is on level ground with out-riggers extended and bog mats in place Ensure that ground load bearing is known to prevent risk of point loading Delivery trucks follow direction of pump operator or hose man |
| Manual handling | Musculoskeletal injuries, | Ensure travel area is free as is practicable from tripping hazards Rotate hose end operator on regular basis |
| Exposure to concrete | Health effects from exposure to concrete | Used as directed and take precautions as on label of SDS Typically, may include: Protective long boots with safety caps Safety glasses Hearing protection Gloves If concrete ingested – seek immediate first aid |
| Clean up before leaving site | Trip, slips, falls, manual handling, security | Clean hoses with appropriate caution, particularly with controlling sponge exit from pipe. Put waste into designated waste area Ensure clean-up of road/footpath or other public area Shutdown and secure all attachments to vehicle |

| Name of Worker/s | Worker signature/s |
| --- | --- |
| Date SWMS received by workers |  |

PLEASE NOTE: It may be necessary to use more than one page to complete an adequate safe work method statement (SWMS).